## Slide 1: INTERREG IIIΑ GREECE-ITALY 2000-2006
Project BIOSIS
Project leader: Prof. G. Lyberatos

## Slide 2: University of Patras, Dept of Biology Microbiology group
Team leader: Assoc. Prof. G. Aggelis
Team members:
Dr S. Fakas, Post-doc researcher
A. Makri, PhD candidate
S. Bellou, A. Kommatas, M. Mavromati
G. Rouni, M. Tselepi, G. Tsoumpeli
Team tasks:
Biotechnological production of biodiesel
By-product valorization

## Slide 3: Biodiesel production
Biodiesel is produced by transesterification of vegetable oils with methanol.
Triacylglycerols (TAG) are the main constituent of vegetable oil, animal fats and microbial lipids.

## Slide 4: Microbial lipids (Single Cell Oil, SCO)
Zygomycetes accumulate lipids rich in unsaturated fatty acids (e.g. γ-linolenic acid - GLA, dihomo-γ-linolenic acid - DHGLA, arachidonic acid - AA) of high nutritional and dietary importance.
Many microorganisms store lipids with unusual composition or structure which presenting composition similarities with various exotic fats (e.g. cocoa butter).
Microbial lipids can be extracted and transformed to biodiesel.

## Slide 5: TAG accumulation by oleaginous m/o grown on glucose

## Slide 6
GLYCEROL
METABOLISM

## Slide 7: Glycerol metabolism in microbial cell
Aerobic
Anaerobic
Prokaryotic
Eukaryotic
Prokaryotic

## Slide 8: Glycerol catabolism in eukaryotic microorganisms

## Slide 9: Substrates used for SCO production
Glucose
Raw glycerol
Pear pomace

## Slide 10
MICROBIAL LIPID PRODUCTION FROM GLUCOSE

## Slide 11
Microorganisms | Biomass (g/l) | Lipid content (w/w %)
Cunninghamella echinulata | 15.0 | 46.0
Mortierella ramanniana | 21.2 | 31.7
Mortierella isabellina | 25.0 | 35.0
Mucor sp | 18.5 | 25.3
Thamnidium elegans | 22.0 | 33.5
Screening of oleaginous fungi on glucose

## Slide 12: Growth and lipid production by Mortierella isabellina on glucose
YX/S
0.35
0.15
YL/S

## Slide 13
MICROBIAL LIPID PRODUCTION FROM GLYCEROL

## Slide 14: Raw or Industrial glycerol
Βy-product of biodiesel production process.
1kg of glycerol becomes available by the production of 10kg biodiesel.
Important feedstock since biodiesel is applied on a large commercial scale.
Enormous amounts of raw glycerol are accumulated.

## Slide 15
Methanol
Soap
Inorganic salts
Glycerol from rapeseed oil contains :
Phosphorus : 1.05 - 2.36 % (w/w).
Potassium : 2.20 - 2.33%.
Sodium : 0.09 - 0.11%.
Traces of cadmium, quicksilver and arsenic.
Raw glycerol contains impurities:

## Slide 16
pure glycerol
raw glycerol
pH 12
raw glycerol
pH 7
raw glycerol pH 7
after centrifiguration

## Slide 17: Raw glycerol valorization
Raw glycerol is used as sole carbon substrate in several biotechnological applications :
Succinic acid by Anaerobiospirillum succiniciproducens.
Ethanol, succinic acid, acetic acid, lactic acid, Η2 etc
by Escherichia coli.
Citric acid by Yarrowia lipolytica.
1,3-propanediol by Clostridium butyricum.
TAG by oleaginous microorganisms.

## Slide 18
Raw Glol
S.C.O.

## Slide 19: Screening of oleaginous fungi on raw glycerol
Microorganisms | Biomass (g/l) | Lipid content (w/w %)
Cunninghamella echinulata | 8.2 | 19.5
Mortierella ramanniana | 7.0 | 22.0
Mortierella isabellina | 6.2 | 53.2
Mucor sp | 7.9 | 19.5
Thamnidium elegans | 20.9 | 38.3

## Slide 20: YX/S YL/S
0.21
Growth and lipid production by
Thamnidium elegans on raw
glycerol
0.08

## Slide 21
Time (h)
Neutral lipids accumulate during growth
Stationary phase
Neutral lipids
Glycolipids+
sphingolipids
Phospholipids
Neutral lipids
Glycolipids+
sphingolipids
Phospholipids
Late exponential phase
Lipids (% w/w of total lipids)
Mid exponential phase
Neutral lipids
Glycolipids+
sphingolipids
Phospholipids

## Slide 22: NEUTRAL LIPIDS GLYCOLIPIDS PHOSPHOLIPIDS & SPHINGOLIPIDS

## Slide 23: Fatty acid composition of Thamnidium lipids in stationary phase

## Slide 24
Fatty acid analysis of Thamnidium

## Slide 25
Scale-up of Thamnidium elegans in laboratory bioreactor
Culture Conditions
Batch cultures on glycerol
Total volume : 3.7 l
Working volume : 2 l
Temperature : 28 oC
Automatic pH regulation at 6.0
Agitation speed : 250-350 rpm
Aeration rate : 1-2 vvm

## Slide 26: Kinetic models for growth and oil accumulation by Thamnidium elegans

## Slide 27
Growth and lipid production by Yarrowia lipolytica on raw glycerol in continuous culture

## Slide 28: Citric acid production by Yarrowia lipolytica on raw glycerol in batch culture

## Slide 29: Raw glycerol vs glucose
Substrate | YX/S (g/g) | YL/S (g/g) | Lipid content (w/w %)
Glucose | 0.35 | 0.15 | 45.0
Industrial glycerol | 0.21 | 0.08 | 43.0

## Slide 30
Culture Conditions
Repeated batch cultures on glycerol
Total volume : 3.7 l
Working volume : 2 l
Temperature : 28 oC
Automatic pH regulation at 6.0
Agitation speed : 350-450 rpm
Aeration rate : 1-2 vvm
Glycerol metabolism in Yarrowia lipolytica

## Slide 31
SOLID STATE FERMENTATION

## Slide 32: Solid state fermentation of Mortierella isabellina on by-products from pear processing

## Slide 33: Lipid production by Mortierella isabellina on by-products from pear processing

## Slide 34
SOLID STATE
FERMENTATION
RENEWABLE CARBON SOURCES
(glucose, xylose, starch,
raw glycerol, tomato waste hydrolysate, pear pomace, industrial fat etc)
40-60% SCO / DW
OR
8-10 % SCO / DB
1-1.2 g/l GLA
40-45 % CBS/DW
8-10 % biodiesel / DW
Notes: <number>

## Slide 35
Notes: <number>